# ARCONA 38

SPECIFICATIONS

Loa	11.45	m

Lwl	9.10	m

Beam	3.50	m

Draught std keel	1.82	m

Keel weight (lead)	2.3	ton

Deplacement	6.90	ton

Fuel tank	90.00	l

Water tank	180.00	l

Holding tank	70.00	l

Engine vp 2030	28.00	hp

7/8-rig			Mast head rig

Main sail	39.00	sqm	main sail	32.00 	sqm

Storm jib	9.00	sqm	storm jib	12.00	sqm

Self tack jib	26.00	sqm	genoa 4	20.00	sqm

genoa 4	17.00	sqm 	genoa 3	32.00	sqm

genoa 3	32.00	sqm 	genoa 2	41.00	sqm

genoa 2	37.00	sqm 	genoa 1	50.00	sqm

genoa 1	42.00	sqm 	furling genoa	45.00	sqm

furling genoa	38.00	sqm 	spinnaker	116.00	sqm

spinnaker	103.00	sqm

Mainsail and selftacker jib included in standard boat.

## General

This specification is valid at the time of printing. Details of the construction, manufacture and equipment may be changed as a result of experiences from production and use of the boats. The standard of quality and equipment will, however, be at least as specified here in.

## Insurance

The yard’s own insurance will cover the boat and other equipment supplied by the builder during the building time until delivery. Owner supplied items to be insured by the same.

## Warranty

The boat has one-year (12 months) warranty against production and material faults. Installed equipment has warranty according to each supplier’s warranty conditions.

## Construction

The hull with integrated bathing platform is built in a sandwich construction of glass fibre reinforced polyester plastic, and with divinicell as a spacer material for strength and insulation. The colour is white and with blue trim and water line.

## The lead keel is bolted on with stainless steel bolts. GRP rudder is mounted on to a 50 mm stainless steel rudderstock. The strong rudder fittings are of cast bronze. The water, fuel and holding tanks are of stainless steel.

## Superstructure

Built of sandwich construction with divinicell as spacing material for strength and insulation. Colour: White. Hull and deck are bolted together. Strengthened glass fibre laminate under the winches, sheet tracks and other stressed areas. Large self-draining locker forward for anchor chain, warps, fenders etc.

## Deck fittings

2 x genoa sheet winches Lewmar 43

2 x halyard winches            “         30

2 lockable winch handles

4 x 25 cm mooring cleats

Pulpit and pushpit in stainless steel

4 pairs of stanchions mounted on stainless steel bases

Double lifelines

2 deck ventilators

2 x 3 m long genoa tracks with 2 sheet blocks

## Mast and rig

Mast in silver anodised aluminium profile 175/126 mm, height 18,1 m, stepped on the keel. The mast is fitted with twin spreaders, steaming light and is prepared for spinnaker equipment. 19-ply stainless steel wire standing rigging, 8 mm top shrouds. 7mm forestay, 6 mm 133-ply stainless steel internal wire/terylene halyards, 5/8 stainless steel rigging screws. Stainless steel chain plates, bolted to longitudinal bulkheads, bonded to hull sides. Boom in silver anodised aluminium profile 165/100 mm with internal outhaul and reefing lines.

## Engine

Volvo Penta 2030 fresh water-cooled marine diesel. Power output at propeller, 28 hp. Instrument panel with rev. counter. Control display for low oil pressure, height engine temperature and charging. Audible warning for oil pressure and water temperature. Volvo Penta S-drive and folding propeller. The engine is easily accessible for service. All hull inlets are fitted with seacocks. All hose clips are in stainless steel.

## Electrical system

12 V 70 amp. hr domestic lighting battery, 14 V a.c. 60 amp. alternator.

12 V 60 amp hr engine battery. Well-dimensioned electrical cables. The cables are to a large extent run in conduits. Main switch panel with circuit breakers. Water and fuel meter, voltmeter/ampmeter. Two main switches, 1 x 12 V power socket.

## Steering

Steering pedestal in GRP, white, with stainless steel wheel and compass. Stainless steel chain and wire cable to a large quadrant. Wheel shaft with adjustable friction brake. Emergency steering on rudder post.

## Cockpit and equipment

Spacious cockpit. Spacious cockpit lockers. Two self-draining recesses in the coamings for winch handles, binoculars etc. Manual type bilge pump. Sprayhood 2 x 32 mm cockpit drains.

## Interior

High standard handcrafted interior in selected and unstained mahogany, varnished to a satin finish. Interior lined in mahogany. Flooring of varnished teak and wholly removable hatches for the bilge, seacocks etc. Headlining of white vinyl covered plastic foam with mahogany strips. Curtains for all portholes. All cushions in high class furnishing fabric. Cupboards and doors properly framed and panelled in mahogany with profile edges.

## Cabins

Large cabins separated from the main saloon by doors. Very comfortable full size double berths. Storage space under berths. Storage cupboards over berths. Reading lamp over each berth.

## Saloon

Spacious and light saloon with full headroom, 196 cm. U-chaped settee to port side, length 210 cm, settee to starboard, length 200 cm (single cabin), 180 cm (double cabin). Behind back rests large storage space. Brass reading lamps. Bookshelves and cupboards. Large storage compartment under the settees Ceiling lights. Large table with drop leaf and bottle locker.

## Navigation area

Large navigation area. Chart table with storage under. Drawers, chart lamp, ample space for electronic equipment.

## Galley

L-shaped galley. Centrally positioned, allowing free passage between the cockpit and saloon. Stainless steel twin sinks. Gimballed twin burner gas cooker with oven. Gaspipes with stop valve and leakage indicator between cooker and gas bottle. Large working areas in easily cleaned and durable laminate. Well insulated refrigerator. Storage compartment for provision. Cupboards for plates, cups and glasses. Bottom cupboard for utensils. Waste basket under sink. Drawers for cutlery. Cutting board. Lights over working areas.

## Fresh and sea water system

Stainless steel water tank (180 l). Electrical freshwater pump. Manual seawater pump.

## Toilet – shower

Large toilet compartment with full headroom and shower facilities. Large recessed washbasin. Sea toilet with holding tank (70 l). Electrical freshwater pump. Mirror, large cupboard, ceiling light. Shower water evacuation pump.

## Two aft cabins version

Two large cabins separated from the main saloon by doors. Large hanging wardrobe, 2 wide full-size double berths. Reading lamps, 2 openable portholes.

## One aft cabin version

Large single cabin separated from the main saloon by door. Large hanging wardrobe, 1 wide full-size double berth, reading lamp, 1 openable porthole. This alternative gives you a very large stowage on the starboard side. The toilet space is also roomier.

## Fittings

Internationally approved navigation lights.

Folding sprayhood

6 portholes in coach roof, 2 portholes in cockpit. All portholes in 6 mm acrylic glass in aluminium frames. Illuminated pedestal mounted compass. Manual bilge pump. Stainless steel transom mounted bathing ladder.

2 x 10 m mooring lines, 4 x 8” fenders. 1 x anchor warp 40 m.

1 x 10 kg Danfort type anchor.

2 x fire extinguisher, 1 x gas bottle.

## Ventilation

Forward cabin:	1 deck hatch

Saloon:	1 deck hatch and 2 ventilators

Aft cabin:	2 opening portholes

Toilet-shower:	1 ventilator

## Extra equipment

The standard Arcona 38 is equipped above. For additional equipment, refer to the price list of option equipment.